## Slide 1: Automated Sensor Testing Prototype
Implementation Plan & Hardware Setup Presenter: Tan Yi Rong

## Slide 2: Prototype Objective
â€¢ The Goal: Build a small-scale, fully functional physical prototype that perfectly mimics the Overhead Hoist Transport (OHT) sensor environment. â€¢ Why We Need It: Before retrofitting 250 vehicles, we must validate the new magnetic connector logic and prove our centralized testing station concept works flawlessly. â€¢ The Scope: Automate the physical 'Detect / No-Detect' environment to eliminate the need for an engineer to manually stand in front of the sensors.

## Slide 3: Structural Architecture
â€¢ The Base Structure: A rigid structure built using standard T-Slot Extruded Aluminum (e.g., 2020 or 3030 series) for maximum modularity and ease of adjustment. â€¢ Sensor Mounting: All 4 OHT sensors will securely mount to the top beam of the aluminum frame, replicating their exact positions on a Mark 2 OHT chassis. â€¢ Calibration: The frame allows slight Z-axis and X-axis adjustments to fine-tune the sensor angles before locking them down.

## Slide 4: Automated Obstacle Simulation
â€¢ The Physical Concept: Instead of an engineer manually blocking the sensors, a large sheet of acrylic serves as the artificial 'obstacle.' â€¢ Distance Accuracy: The rig is calibrated to mimic an obstacle exactly 1.5 meters away from the mounted sensors. â€¢ Automated Movement: The acrylic sheet is programmed to slide Left/Right and Up/Down, triggering the sensors sequentially to generate live data.

## Slide 5: Required Hardware & Motors
â€¢ Linear Motion: 2x Linear Guide Rails (with carriage blocks) ensure the acrylic sheet slides smoothly without vibration. â€¢ Actuation (Motors): 2x NEMA 17 Stepper Motors (X-axis, Y-axis) provide precise, programmable control over the acrylic sheet. â€¢ Drive System: GT2 Timing Belts and Pulleys connect to the stepper motors. â€¢ The Target: 1x Matte or Tinted Acrylic Sheet (blocks sensors without reflecting stray light).

## Slide 6: Electrical & Wiring Architecture
â€¢ Motor Control: An Arduino Uno paired with a CNC Shield and A4988 Stepper Drivers executes the programmed movement. â€¢ Sensor Wiring: The 4 sensors on the frame wire down into the proposed Centralized Relay Station. â€¢ Magnetic Plug Test: The relay station routes through our prototype PCB Bridge Board, connecting to a sample OEM Magnetic 15-Pin Plug.

## Slide 7: Budget Justification
â€¢ Items to Purchase: T-Slot Aluminum Extrusions, 2x NEMA 17 Motors + Rails, Arduino Kit, 4-Channel Relay Module, OEM Plug Samples, Acrylic Sheet. â€¢ Justification: Procuring these low-cost Maker components (est. <SGD 300) validates the centralized relay logic and magnetic plug alignment. â€¢ ROI: This minimal upfront cost unlocks our SGD ~42k fleet retrofit strategy, definitively proving a >SGD 100k cobot is entirely unnecessary.

## Slide 8: Full System Integration (The Loop)
â€¢ The DIY Coordinate Robot: I will construct a low-cost Cartesian robot arm. Because the magnetic plug is self-aligning, this DIY arm only needs 'blind' coordinate movement to plug in and out - no camera vision required! â€¢ The Seamless Loop: 1. The DIY arm snaps the magnetic plug into the testing port. 2. C# PM Simulator commands the acrylic sheet to simulate an obstacle. 3. Simulator successfully detects the obstacle; Central Relay instantly switches power to the next sensor. 4. Acrylic sheet shifts to the new sensor, entirely automating the manual PM test!