## Slide 1: Robot Arm Project Proposal
OHT Mark 2 PM Workflow Simulator Presenter: Tan Yi Rong Date: July 2026

## Slide 2: Project Objective
Current State: The PM sensor connection is manual, labour-intensive, and prone to human error. Proposed Solution: Integrate a Collaborative Robot (Cobot) arm to automatically handle the sensor plug connection to the OHT. Goal: Reduce operational downtime, eliminate manual alignment errors, and enable a fully automated, vision-assisted PM workflow.

## Slide 3: Vendor Comparison
OMRON (TM5S Series): Built-in vision, 900mm reach, SGD 100k - 150k. Universal Robots (UR7e): No camera, ~730mm reach, ~SGD 29k - 36k. ABB (GoFa): Advanced torque sensors, up to 950mm reach, SGD 40k - 70k. Takeaway: The extreme budget constraints require us to explore internal engineering alternatives instead of procuring premium hardware.

## Slide 4: The Core Challenge
The Problem: The primary driver of the high vendor quotations is the requirement for a highly precise Robot Vision System. Why Vision is Needed: The current OHT sensor uses a complex 4-port plug. A robot arm without a camera cannot accurately align and insert a 4-pin connector just by 'feel'. The Crossroads: Do we heavily increase the project budget for vision-assisted robots, or do we redesign the hardware to eliminate the need for vision entirely?

## Slide 5: Hardware Redesign: Magnetic Connector
The Concept: Replace the complex 4-port plug with a centralized single magnetic connector. Eliminating Vision: Magnetic connectors auto-align themselves via magnetic pull. A low-cost, DIY robot arm only needs to bring the plug close to the port, and magnets will snap it into perfect alignment automatically. Cost Efficiency: This drastically drops the robotics budget, allowing us to build an in-house DIY arm.

## Slide 6: Fleet Retrofit Cost Analysis
Implementation Considerations for 250 OHT Vehicles: Magnetic 15-Pin Plug (Premium Rosenberger): SGD 17,500 (Alternative) Cheaper OEM Plug: ~SGD 3,750 Custom PCB Breakout & Relays: ~SGD 2,000 Mounting Brackets & Labor: ~SGD 23,750 GRAND TOTAL (Premium Plug): ~SGD 42,550 GRAND TOTAL (Cheaper OEM Plug): ~SGD 28,800

## Slide 7: Sourcing & PCB Implementation
Vendor Pricing Comparison: Rosenberger (Germany): Premium / Aerospace Grade (~SGD 70.00) C.C.P. Contact Probes (Taiwan): High Industrial Grade (~SGD 25.00) HytePro / Top-Link (China): Standard OEM Pogo-Pin (~SGD 15.00) Installation Mechanics (PCB Bridging): The Bridge Board: We will design a tiny, custom PCB (SGD 3 each) to seamlessly map the magnetic pins to our standard wires.

## Slide 8: Next Steps & Conclusion
Finalize the budget review and formally reject the current OMRON / UR / ABB vendor quotations. Draft the electrical schematic for the proposed central testing station relay circuit. Procure sample magnetic connectors from OEM manufacturers to test alignment strength. Conclusion: By intelligently redesigning the physical connector and centralizing the relay logic, we bypass expensive robot vision requirements and achieve massive cost savings for the automation project.